## Slide 1
Lab Book 0.1. ModeSolver
Student:

## Slide 2: Instructions General
SCRIPTS
From GitHub 
  Fork the repo: https://github.com/cccanvas-upv/pic-upv-lab0.git
  Clone the repo using VSCode
Run the Jupyter Notebook:
  010_MODESOLVER_Student.ipynb
INSTRUCTIONS
We are going to work with different Cross-Sections. In general, we will need: Materials definitions and the Geometrical parameters of each Cross-section.
XY Cross-section
h
(height)
W (width)
Core
Cladding
W (width)
Core
Cladding
Slab
h_slab
h_core
shallow waveguide
deep waveguide

## Slide 3: Learning outcome #1 – Effective index of a waveguide
INSTRUCTOR:
Present Python and GDSFactory: materials, output, results.
Explain how to run a simulation for a particular cross-section.
Showcase how to change between shallow and deep waveguide.
Describe how to change the wavelength and width for the waveguide analysis.
Describe the outputs.
ALL EXAMPLE #1: waveguide width 1.2 µm, deep wvg, wavelength start and end same 1.55 µm  all ”Run”
ALL: Follow instructor, that will show how to 1) plot mode, 2) explore the results (neff …)
Document all your results (neff, plot fields of different modes, comparison between different polarizations…)

## Slide 4: Learning outcome #2 – Wavelength behavior Wavelength 1.5-1.6 µm (step 0.02 µm) – width 1.2 µm
Comment results (neff changes this way with wavelength, comparison between different waveguide cross-sections …)
En la guia shallow los modos viajan más confinados al tener una sección de core más ancha, también consigue propagar más modos con el modo fundamental TE0, el primer modo TM, el Segundo es híbrido ya que la fracción TE es el 66% y tercero TE. En la guia deep, a pesar de que te encuentra 4 soluciones, te las encuentra porque le fuezas a ello, pero solo las dos primeras se propagan, tal como se ve en la gráfica. El modo 0 es TE y el primero TM
shallow waveguide
Paste plot here
deep waveguide
Paste plot here
slab = 150nm

## Slide 5: Thank you